## Slide 1: A Study to reduce the re-autoclave rate at the CSSD of Sitaram Bhartia Institute of science and research
Student Name- Yashwardhan Kakkar
Mentor Name- Dr. Altaf Yousuf Mir
Enrolment No.- PG/22/140
IIHMR Delhi

## Slide 2: Mentor Approval

## Slide 3: Introduction
CSSD in hospitals are responsible for providing sterilized instruments to various departments like OT, NICU, PICU, etc. for aseptic processes.
At CSSD, sets are firstly pre-cleaned in dirty zone, then dried, packed and put for autoclaving in the packing and autoclaving zone.
The sterilized instruments before autoclaving are packed in either :
  Casement cloth (7 days shelf life)
  SMS sheet (3 month shelf life)
  Medical grade paper (6 month shelf life)
After that sets are stored in the clean area and are issued from there only.

## Slide 4: Need for the study
To ensure patient safety and the efficient functioning of healthcare institutions, the Central Sterile Services Department (CSSD) must handle sterilization procedures with efficiency.
Re-autoclave rate of 14-15% in the month of February, March and April.
Recurring problem of re-autoclaving raise the possibility that the packaging and sterilization practices in use today are insufficiently effective.
The efficiency of the CSSD's sterilization procedures can be enhanced by recognizing and resolving these problems.

## Slide 5: Objectives
To decrease the re-autoclave rate in the CSSD of Sitaram Bhartia Hospital
To investigate the causes of re-autoclave cases in CSSD.
To increase CSSD efficiency by decreasing the cost, manpower hours associated with re-autoclaving of medical instruments.

## Slide 6: Methodology
Study design: Prospective study.
Study area: The study is being done in the Central sterile services department (CSSD) of Sitaram Bhartia institute of science and research.
Data Collection: Through CSSD registers, EMR and random audits at CSSD.

## Slide 7: Methodology
Sample Size: All the medical instrument sets sterilized at CSSD from the month of February to June.
Timeframe: 3 Months
  April- Pre study to analyze the problem and start collecting data
  May and June- Changes implementation and Analysis.

## Slide 8: Results
Monthly Re-autoclave Data: 391 sets in February, 397 sets in March, 342 sets in April.
Re-autoclave Rates: 15% in February and March, 14% in April.
Efficiency Impact: High re-autoclave rate reduces CSSD efficiency.
Cost Implications: Re-autoclaving increases costs (electricity, water, materials).
Recommendations: Implement CSSD protocols to reduce re-autoclave rates, boost efficiency, and lower costs.

## Slide 9: Results
Packing Sheets Distribution: 72% of Re-Autoclaved sets are packed in Casement sheets, 19% in SMS sheets and 9% in medical grade sheets.
Shelf Life: Casement sheets have a 7-day shelf life, while medical grade and SMS sheets have a 30-day shelf life in Sitaram Bhartia Hospital.
Re-autoclave Rates: High re-autoclave rate linked to casement sheets due to their shorter shelf life.
Interviews with Nurses: Identified infrequently used sets packaged in casement sheets.
Shift to SMS Sheets: Repackage identified sets in SMS sheets for longer shelf life.

## Slide 10: Results
Manpower Issues: Incomplete drying of instruments leads to damp conditions requiring re-autoclaving
Machine Problems: Positive Bowie Dick test results necessitate re-autoclaving all previous sets.
Methodological Flaws: Noncompliance with FIFO and non standardized packaging protocols increase re-autoclaving events.
To tackle this proper protocols are created regarding what sets to pack in what type of packaging and nurses are instructed to follow FIFO process.
Material Concerns: Packaging materials providing less shelf life as compared to standardized.
To increase the shelf life from 30 to 45 days, culture report is being sent after 45 days to check any microbial growth and no growth was found and sterility was maintained

## Slide 11
Results
Initiation of Changes: Changes were initiated in the month of may.
A slight dip in the re-autoclave rate was observed from 15% to 12%.
After all the changes were implemented, a significant drop in the re-autoclave rate was observed to 9% by the mid of June.
This drop demonstrates the importance of having standard procedure to increase the efficiency of the department.
Reduction in re-autoclave rate will let the staff to focus more on value adding activities rather than autoclaving instruments again and again.

## Slide 12: Discussion
Study highlighted the crucial need for systematic improvements in sterilizing procedures within healthcare settings.
Significant inefficiencies, such as a high re-autoclave rate of around 15% in the initial three months, were identified.
Using tools like the Fishbone Diagram, several critical causes, including staffing issues, machinery breakdowns, procedural lapses, and improper packaging material use were observed.
Under-drying of instruments, before autoclaving, not having standardized protocols, non-adherence to FIFO procedure, less shelf life of sets, underscores the necessity for rigorous training and standardized protocols in the CSSD.

## Slide 13: Discussion
After implementation of various improvements, including enhanced packing techniques and the extension of shelf lives of medical instrument sets, the re-autoclave rate is being decreased to 9%.
Our study indicates that addressing complex issues with improved protocols, training, and material management strategies can substantially enhance operational efficiency and patient safety.
Further more reduction in the re-autoclave rate can be observed as the shelf life can be increased to 90 days for SMS sheets and up to 6 months for Medical grade paper.

## Slide 14: Conclusion
Pre study indicates high re-autoclave rate of around 15% in the month of February, March and April.
Major causes of high re-autoclave rate was because of lack of standardized protocols, non adherence proper process flow and less shelf life of medical instrument sets.
A significant reduction from 15% to 9% is being observed in the re-autoclave rate by the mid of June.

## Slide 15: References
Guidelines for central sterile supply department (cssd) & mechanized laundry ministry of health & family welfare government of India [internet]. 2023. Available from: https://nhsrcindia.org/sites/default/files/Guidelines- on-CSSD-and-Mechanised-Laundry.pdf
Decontamination and Reprocessing of Medical Devices for Health-care Facilities [Internet]. 2016. Available from: https://iris.who.int/bitstream/handle/10665/250232/9789241549851-eng.pdf?sequence=1
Rutala WA, Weber DJ. Guideline for Disinfection and Sterilization of Prion-Contaminated Medical Instruments. Infection Control & Hospital Epidemiology [Internet]. 2019;31(2):107–17. Available from: https://www.cdc.gov/infectioncontrol/pdf/guidelines/disinfection-guidelines.pdf
Prevention of hospital-acquired infections A practical guide 2nd edition [Internet]. World Health Organization; 2012. Available from: https://iris.who.int/bitstream/handle/10665/67350/WHO_CDS_CSR_EPH_2002.12.pdf
Ensuring critical instruments and devices are appropriate for reuse [Internet]. 2022 Feb [cited 2024 May 9]. Available from: https://www.jointcommission.org/-/media/tjc/documents/resources/patient-safety-topics/infection-prevention-and-hai/2024/quick-safety-64-reuse-of-critical-instruments-2-14-22-final4.pdf

## Slide 16: Thank You

## Slide 17: Pictorial Journey

## Slide 18: Pictorial Journey